## Slide 1
L2 Signals

## Slide 2
ANALOG AND DIGITAL DATA
Data can be analog or digital.
The term analog data refers to information that is continuous;
digital data refers to information that has discrete states.
Analog data take on continuous values. Digital data take on discrete values.
Data: Entities that convey meaning or information

## Slide 3: Analog and Digital Signals
Signals can be analog or digital.
Analog signals can have an infinite number of values in a range.
Digital signals can have only a limited number of values.

## Slide 4: Analog and Digital Signals
Electric or electromagnetic representations of data
Analog signal is continuously varying electromagnectic wave
Digital signal is sequence of voltage pulses
Digital signals generally cheaper and less effected by disturbances (noise)
Digital signals suffer more from signal weakening (attenuation)

## Slide 5
Figure 3.1 Comparison of analog and digital signals

## Slide 6
Analog Signaling of Analog and Digital Data

## Slide 7
Digital Signaling of Analog and Digital Data
a device that can both transmit and receive communications
A codec is a device or computer program which encodes or decodes a data stream or signal.

## Slide 8
Ananlog/Digital Signals and Data
Spectrum refers to the invisible radio frequencies that wireless signals travel over.

## Slide 9: Analog vs Digital Transmission
Analog transmission: analog signal is propagated through amplifiers
Digital transmission: analog or digital signals are propagated through repeaters
Digital transmission is preferred technology today: digital equipment, efficiently combine signals from different sources; security; repeaters can give more accurate data transmission

## Slide 10: Examples of Periodic Signals
Any signal is either periodic (the following two) or aperiodic

## Slide 11: Examples of aperiodic signals
Any signal is either periodic (the following two) or aperiodic

## Slide 12
3-2 PERIODIC ANALOG SIGNALS
In data communications, we commonly use periodic analog signals and nonperiodic digital signals.
Periodic analog signals can be classified as simple or composite. A simple periodic analog signal, a sine wave, cannot be decomposed into simpler signals.
A composite periodic analog signal is composed of multiple sine waves.

## Slide 13
Figure 3.2 A sine wave

## Slide 14
Figure 3.3 Two signals with the same phase and frequency, but different amplitudes

## Slide 15: Frequency
Frequency is the rate of change with respect to time.
Change in a short span of time means high frequency.
Change over a long span of time means low frequency.
If a signal does not change at all, its frequency is zero.
If a signal changes instantaneously, its frequency is infinite.

## Slide 16
Frequency and period are the inverse of each other.
Note

## Slide 17
Figure 3.4 Two signals with the same amplitude and phase, but different frequencies

## Slide 18
Table 3.1 Units of period and frequency

## Slide 19
The power we use at home has a frequency of 60 Hz. The period of this sine wave can be determined as follows:
Example 3.1

## Slide 20
The period of a signal is 100 ms. What is its frequency in kilohertz?
Example 3.2
Solution
First we change 100 ms to seconds, and then we calculate the frequency from the period (1 Hz = 10−3 kHz).

## Slide 21
Figure 3.5 Three sine waves with the same amplitude and frequency, but different phases
Phase describes the position of the waveform relative to time 0.

## Slide 22
A sine wave is offset 1/6 cycle with respect to time 0. What is its phase in degrees and radians?
Example 3.3
Solution
We know that 1 complete cycle is 360°. Therefore, 1/6 cycle is

## Slide 23
Figure 3.6 Wavelength and period
While the frequency of a signal is independent of the medium, the wavelength depends on both the frequency and the medium.
The wavelength is the distance a simple signal can travel in one period. (usually, unit of measurement is meters)

## Slide 24
Figure 3.7 The time-domain and frequency-domain plots of a sine wave
A complete sine wave in the time domain can be represented by one single spike in the frequency domain

## Slide 25
Figure 3.8 The time domain and frequency domain of three sine waves
frequency domain is more compact and useful when we are dealing with more than one sine wave

## Slide 26: Signals and Communication
A single-frequency sine wave is not useful in data communications
We need to send a composite signal, a signal made of many simple sine waves.
According to Fourier analysis, any composite signal is a combination of simple sine waves with different frequencies, amplitudes, and phases.

## Slide 27: Composite Signals and Periodicity
If the composite signal is periodic, the decomposition gives a series of signals with discrete frequencies.
If the composite signal is nonperiodic, the decomposition gives a combination of sine waves with continuous frequencies.

## Slide 28
Figure 3.10 Decomposition of a composite periodic signal in the time and frequency domains

## Slide 29
Figure 3.11 The time and frequency domains of a nonperiodic signal

## Slide 30: Spectrum and Bandwidth
The spectrum of a signal is the range of frequencies contained in the signal.
The bandwidth is the difference between the lowest and highest frequency in the spectrum.
Bandwidth is subset of Spectrum

## Slide 31
Figure 3.12 The bandwidth of periodic and nonperiodic composite signals

## Slide 32
If a periodic signal is decomposed into five sine waves with frequencies of 100, 300, 500, 700, and 900 Hz, what is its bandwidth? Draw the spectrum, assuming all components have a maximum amplitude of 10 V.
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
Example 3.6
The spectrum has only five spikes, at 100, 300, 500, 700, and 900 Hz (see Figure 3.13).

## Slide 33
Figure 3.13 The bandwidth for Example 3.6

## Slide 34
A periodic signal has a bandwidth of 20 Hz. The highest frequency is 60 Hz. What is the lowest frequency? Draw the spectrum if the signal contains all frequencies of the same amplitude.
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
Example 3.7
The spectrum contains all integer frequencies. We show this by a series of spikes (see Figure 3.14).

## Slide 35
Figure 3.14 The bandwidth for Example 3.7

## Slide 37
.
Composite Signals
A composite signal can be periodic or nonperiodic.
A periodic composite signal can be decomposed into a series of simple sine waves with discrete frequencies that have integer values (1, 2, 3, and so on).
A nonperiodic composite signal can be decomposed into a combination of an infinite number of simple sine waves with continuous frequencies, frequencies that have real values.

## Slide 38
.
Composite Signals
The amplitude of the sine wave with frequency f is almost the same as the peak amplitude of the composite signal.
The amplitude of the sine wave with frequency 3f is one-third of that of the first, and the amplitude of the sine wave with frequency 9f is one-ninth of the first.

## Slide 39
.
Composite Signals
The frequency of the sine wave with frequency f is the same as the frequency of the composite signal; it is called the fundamental frequency, or first harmonic.
The sine wave with frequency 3f has a frequency of 3 times the fundamental frequency; it is called the third harmonic.
The third sine wave with frequency 9fhas a frequency of 9 times the fundamental frequency; it is called the ninth harmonic.

## Slide 40
.
Composite signals can be expressed as a combination of simple sine waves with different amplitude, frequency and phase.
s (t ) = A1 sin (2πf1t + φ1) + A2 sin (2πf2t + φ2) + A3 sin (2πf3t + φ3) +……..

## Slide 41
.
Digital signal
Most digital signals are nonperiodic
period and frequency are not appropriate characteristics.
Bit interval
Time required to send a single bit.

## Slide 42
.
Digital signal
Bit Rate
Number of bits sent in 1 second, expressed in bits per second (bps).
Number of bit intervals per second.

## Slide 43: Digital Signals
Bit interval(T): It is the time required to send a single bit.
Bit rate: It is number of bit intervals per second.(1/T)
Propagation time: It is the time required for signal to travel from one point of transmission medium to another.
Propagation time=Distance/ Propagation speed

## Slide 44
.
Digital signal
A digital signal can have more than two levels.
In this case, we can send more than 1 bit for each level.
In general, if a signal has L levels, each level needs log2L bits.

## Slide 45
Example 3.17
A digital signal has nine levels. How many bits are needed per level?
Each signal level is represented by 3.17 bits.
The number of bits sent per level needs to be an integer as well as a power of 2.
4 bits can represent one level.

## Slide 46
.
DIGITAL SIGNALS
Digital Signal as a Composite Analog Signal
Fourier analysis can be used to decompose a digital signal.
If the digital signal is periodic, (rare in data communications ), the decomposed signal has a frequency domain representation with an infinite bandwidth and discrete frequencies.
If the digital signal is nonperiodic, the decomposed signal still has an infinite bandwidth, but the frequencies are continuous.

## Slide 47
Book Referred:
Title: Data Communications And Networking
Author: Behrouz A. Forouzan
Chapter: Chapter 3, Data and Signals